## Slide 1
Ch.10 The z-Transform
1. The z-Transform (Ch.10.1)
2. The Region of Convergence for z-Transform (Ch.10.2)
3. The Inverse z-Transform (Ch.10.3)
4. Properties of z-Transform (Ch.10.5)
5. Analysis of LTI systems using z-Transform (Ch.10.7)
6. System Function Algebra and Block Diagram
7. Unilateral z-Transform (Ch.10.9)
Note: complex domain analysis for discrete-time, but what properties for discrete-time complex exponential signals?

## Slide 2
Periodicity Properties of Discrete-time Complex Exponentials e j0n (periodic or aperiodic)
For discrete-time complex exponential signals, only need to consider a frequency interval of 2.
Lowest oscillation rate
Highest oscillation rate

## Slide 3
Difference between LT and z-Transform?
Difference between continuous-time and discrete-time:
For discrete-time signal, its spectrum is periodic with 2
s-plane is replaced with z-plane, still a complex plane
Question: where is the discrete-time Fourier transform on the z-plane with a periodic structure?
Ch.10 The z-Transform

## Slide 4
Review from Chapter 3 (Fourier series)
h[n]
y[n]=H(z)zn
System function
--- z-transform of h[n].
Ch.10 The z-Transform
For any complex number with converging summation
if converging on r = 1
Connection with DTFT, or the frequency response:
if converging on Im
For LT

## Slide 5
Basic requirements:
1. Definition of z-Transform
2. Concept of ROC: difference from LT
3. Commonly-used ZT pairs
4. How to find the ZT of a signal
5. Concept of zeros and poles
1. The z-Transform
Note: be careful with the difference between LT and ZT

## Slide 6
(1) Definition
(2) Definition based on Fourier transform
DTFT
Write z in polar-axis as
determines the convergence.
1. The z-Transform
Note: The ROC is only determined by r, the radius of z.

## Slide 7
(3) Region of Convergence ( ROC )
ROC: Range of values of z for X(z) to converge
Representation: A. Inequality
B. Region in z-plane
1
-1
a
Re
Im
unit circle
Always a circular ROC in the z-plane.
ROC is only determined by r, the radius of z.
1. The z-Transform

## Slide 8
(4) Relationship between discrete-time Fourier transform and z-transform
Very important z-Transform pairs:
If the ROC includes the unit circle |z| = 1.
1. The z-Transform
Note: the same ZT expression, but different ROC’s. Only one of them has FT transform

## Slide 9
Example 10.1: Find z-transform of
Solution:
The condition of convergence:
or
Finished?
NO! Don’t forget the ROC.
1. The z-Transform

## Slide 10
Example 10.1:
1).
2).
Note: which parameter determines the ROC?

## Slide 11
Note the following:
The ROC consists of circular rings centered around the origin
If | a | < 1, x[n] is absolutely summable and has DTFT; also, the ROC for X(z) includes the unit circle.
If the DTFT exists, then
Example 10.1:

## Slide 12
Example 10.2: Find z-transform of
Solution:
The condition of convergence:
or
1. The z-Transform

## Slide 13
Example 10.2:
1).
2).

## Slide 14
From the above two examples, we know that
Like the Laplace transform, two different discrete-time signals might have the same expression for their z-transforms. The only difference is from the different ROC’s.
Both forms might be used.
1. The z-Transform
Right-sided
Left-sided
outside
inside

## Slide 15
Group discussion:
1. Given an LTI system with , determine the possible output signal if the input signal is
2. Given an LTI system with , determine the possible output signal if the input signal is

## Slide 16
Example 10.3: Find z-transform of
Solution:
z-Transform is linear.
1. The z-Transform
ROC for both terms to converge

## Slide 17
After simplification, we obtain
rational form
Example 10.3 (Cont’d):
zeros --- roots of numerator polynomial and X(z) = 0;
poles --- roots of denominator polynomial and X(z) = infinity.
Pole-zero plot: polynomial of z, not z-1
Note that there might exist poles or zeros at infinity.

## Slide 18
Example 10.3:
Two poles at z = 1/3 and z = 1/2;
Two zeros at z = 0 and z = 3/2.
Pole-zero plot:
1/2
1
ROC includes the unit circle, DTFT exists.

## Slide 19
Example 10.4: Find z-transform of
Solution:
Note: the ROC is determined by |a|.

## Slide 20
Example 10.4 (Cont’d):
Two poles:
Two zeros: one at z = 0 and another at z = infinity.

## Slide 21
Example 10.4 (Cont’d):
Pole-zero plot:
ROC includes the unit circle, DTFT exists.
1/3
1
Real signal: poles in conjugate pair

## Slide 22
Note that: some discrete-time signals do not have ZT
The two ROC don’t overlap.
Time-domain:
z-domain:
1. The z-Transform
Another example:

## Slide 23
Summaries:
1. Definition of z-Transform and its connection with DTFT, system function
2. Concept of ROC and its importance
3. Commonly-used ZT pairs
4. How to find the ZT of a signal
Linear property of ZT, ROC intersection
5. ZT in rational form
6. Concept of zeros and poles
1. The z-Transform

## Slide 24
1
-1
a
Re
Im
S-plane:
Z-plane:
jω-axis:
Unit circle
Left plane:
Inside unit circle
Right plane:
Outside unit circle

## Slide 25
LT and ZT:
1. The z-Transform
Poles:
Re
Im
0
Poles:
Mapping:
Re
Im

## Slide 26
LT and ZT: unit impulse sampled signals
1. The z-Transform

## Slide 27
Group discussion:
1. For the signal , its z-transform has ( ) number of zeros in the finite z-plane.
2. For the signal , the ROC of its z-transform is ( ).

## Slide 28
2. The Region of Convergence for z-Transform
For DTFT, we need absolutely sumable for its convergence; here, we need to study the ROC.
Basic requirements:
Based on the properties of ROC, can determine the ROC of a signal’s ZT from its time-domain property (four types of signals).
Understanding and flexible usage of the properties
Should focus on the difference between ZT and LT.

## Slide 29
Property 1: The ROC of X(z) consists of a ring in the z-plane centered about the origin.
Property 2: The ROC does not contain any poles. (Because at the pole, X(z) = infinity.)
(Since the convergence is determined by r.)
2. The Region of Convergence for z-Transform

## Slide 30
Property 3: If x[n] is of finite duration, then the ROC is the entire z-plane, except possibly at z = 0 and/or z = ∞.
0
1
Why the red part in property 3?
It is clearly a signal of finite duration.
Example 10.5:
The ROC:
the entire z-plane.
2. The Region of Convergence for z-Transform

## Slide 31
Example 10.5 (Cont’d):
Finite duration, but a pole at z = 0, so ROC:
1
1
Finite duration, but a pole at z = infinity, so ROC:
Note: time shifting will not change the ROC of Laplace transform.

## Slide 32
Any non-zero impulse in negative time gives pole at z=infinity since X(z) = infinity for that term, for example x[-2]z2;
Any non-zero impulse in positive time gives pole at z=0 since X(z) = infinity for that term, for example x[2]z -2.
2. The Region of Convergence for z-Transform

## Slide 33
However, not necessarily the boundary!
r0
Property 4: If x[n] is a right-sided sequence, and if the circle |z| = r0 is in the ROC, then all finite values of z for which |z| > r0 will also be in the ROC.
2. The Region of Convergence for z-Transform
Why only finite values of z ? May not include z = .

## Slide 34
Property 4: If x[n] is a right-sided sequence, and if the circle |z| = r0 is in the ROC, then all finite values of z for which |z| > r0 will also be in the ROC.
2. The Region of Convergence for z-Transform

## Slide 35
However, not necessarily the boundary!
r0
Property 5: If x[n] is a left-sided sequence, and if the circle |z| = r0 is in the ROC, then all values of z for which 0 < |z| < r0 will also be in the ROC.
2. The Region of Convergence for z-Transform

## Slide 36
Property 6: If x[n] is two-sided, and if the circle |z| = r0 is in the ROC, then the ROC will consist of a ring in the z-plane that includes the circle |z| = r0.
Check the properties with
Example 10.6 10.7
r0
2. The Region of Convergence for z-Transform

## Slide 37
Example 10.6:
Finite duration, ROC is the entire z-plane except N-1-order pole at z = 0.
z = a looks like another pole, but not.
2. The Region of Convergence for z-Transform
N-1 zeros:

## Slide 38
Example 10.6:
2. The Region of Convergence for z-Transform
N-1 zeros:
Discrete-time square wave: a = 1

## Slide 39
Example 10.7:
A two-sided sequence, write it as sum of a right-sided sequence and a left-sided sequence
If b > 1, then the two ROC’s have no overlap, and the z-transform does NOT exist.
2. The Region of Convergence for z-Transform

## Slide 40
b
1/b
1
Example 10.7 (Cont’d):
If b < 1, then the two ROC’s have overlap, and the z-transform exists.
ROC includes the unit circle, DTFT exists.
Property 7: If the z-transform X(z) of x[n] is rational, then its ROC is bounded by poles or extends to infinity.

## Slide 41
Property 8: If the z-transform X(z) of x[n] is rational, and if x[n] is right sided, then the ROC is the region in the z-plane outside the outermost pole --- i.e., outside the circle of radius equal to the largest magnitude of the poles of X(z). Furthermore, if x[n] is causal, then the ROC also includes z = . (If x[n] is causal, the signal is always zero for negative time.)
2. The Region of Convergence for z-Transform
Causal
Non-causal

## Slide 42
Property 9: If the z-transform X(z) of x[n] is rational, and if x[n] is left sided, then the ROC is the region in the z-plane inside the innermost nonzero pole --- i.e., inside the circle of radius equal to the smallest magnitude of the poles of X(z) other than any at z = 0 and extending inward to and possibly including z = 0. In particular, if x[n] is anticausal, then the ROC also includes z = 0.
2. The Region of Convergence for z-Transform
Anti-causal
Non anti-causal

## Slide 43
Example 10.8:
Note that both numerator and denominator should be in polynomials of z, not z-1, thus,
Two poles at z = 1/3, z = 2; and a 2nd-order zero at z = 0.
1. One way to define zeros and poles is to use the definition:
Find its poles and zeros and discuss possible ROC.
No poles or zeros at infinity.

## Slide 44
2. Another way:
To get X(z) = infinity,
To get X(z) = 0,
Example 10.8:
2
1/3
1
Causal

## Slide 45
2
1/3
1
Anti-causal
Example 10.8:
2
1/3
1
Two poles give three possible ROC’s, each one of them corresponds to a different signal.
Two-sided with DTFT

## Slide 46
Summaries:
ROC: circular ROC around origin
Four different types of signals, correspond to four different types of ROC
For rational ZT, ROC is bounded by poles
Causal and anti-causal signal vs. right-sided and left-sided signals
Different from LT, be careful with poles at 0 or infinity
2. The Region of Convergence for z-Transform

## Slide 47
Group discussion:
1. For the signal , the ROC of its z-transform is ( )
2. For the following absolutely sumable signal with X(z), the signal is ( )

## Slide 48
3. The Inverse z-Transform
Basic requirements:
Understanding the concept of inverse ZT: a contour integral in the ROC;
Inverse ZT based on partial fraction expansion
Expand X(z) in polynomials

## Slide 49
Note: 1) the integral is done within any 2π interval
2) any fixed r within the ROC could be used
3. The Inverse z-Transform
Write X(z) as a DTFT with suitable chosen magnitude:
Based on the one-to-one mapping property of FT:

## Slide 50
In general
Fix r and change ω in 2π period, is a circle in the z-plane inside the ROC.
3. The Inverse z-Transform

## Slide 51
The calculation for inverse z-transform:
(1) Integration of complex function.
(2) Compute by partial fraction expansion.
ROC outside the pole
ROC inside the pole
Here, expansion with z-1
3. The Inverse z-Transform

## Slide 52
Example 10.9:
Partial fraction expansion with z-1
3. The Inverse z-Transform

## Slide 53
Example 10.9 (Cont’d):
For both terms, the ROC |z| > 1/3 is an outside ROC. So, both terms are right-sided sequences.
ROC outside the pole
ROC inside the pole
Causal and DTFT exists.

## Slide 54
Example 10.10:
Example 10.11:
3. The Inverse z-Transform

## Slide 55
(3) Expand X(z) in polynomial in z-1
Example 10.12:
3. The Inverse z-Transform
ROC?
Both z = 0 and infinity are poles:

## Slide 56
Example 10.13:
Inside ROC, we have |az-1| < 1, so we can do an expansion as
Inside the ROC, |az-1| > 1, how to do the expansion?
However, for
3. The Inverse z-Transform

## Slide 57
Example 10.13 (Cont’d):
Instead, |a-1z| < 1, so we can do an expansion as
Key: how to do the expansion inside the ROC.

## Slide 58
Example 10.14:
log(1+v) has a nice Taylor expansion as
Inside the ROC, we have |az-1| < 1, so we have
3. The Inverse z-Transform

## Slide 59
Partial fraction expansion or polynomial expansion
Determine the ROC of the ZT: poles and other conditions;
Partial fraction expansion of the ZT
For each term, do the inverse ZT with the determined ROC based on
Summaries:
ROC outside the pole
ROC inside the pole
3. The Inverse z-Transform

## Slide 60
Extra examples:
Given
and x[n] has DTFT , determine x[n].
2. Given and
determine x[n].
3. The Inverse z-Transform

## Slide 61
10.4.1 First-order systems
10.4.2 Second-order systems
10.4 Geometric Evaluation of DTFT
Please read this part yourself.

## Slide 62
Group discussion:
1. Do partial fraction on , the result is ( )
2. Do the inverse ZT for the following signal if the signal has DTFT.

## Slide 63
4. Properties of z-Transform
Basic requirements:
1. Understanding each property: how the time change affects both X(z) and its ROC;
2. Flexible usage of the properties:
Computing ZT, inverse ZT
Determine the ROC
LTI system analysis
……

## Slide 64
1). Linearity:
Note that the ROC of x[n] is at least the intersection of R1 and R2. It could be empty, and it could be larger than the intersection.
Change in the ROC is also important.
With ROC containing R1 ∩ R2,
NOT ROC = R1 ∩ R2
4. Properties of z-Transform
Why?
Pole-zero cancellation

## Slide 65
1). Linearity:
With ROC containing R1 ∩ R2
Note: only works for sum with finite terms.
Pole-zero cancellation:

## Slide 66
2). Time shifting:
with ROC = R, except for the possible addition or deletion of the origin or infinity.
n0 > 0,
Poles introduced at z=0
4. Properties of z-Transform
One pole at z = a
One pole at z =0
One pole at z = a
One zero at z =0

## Slide 67
2). Time shifting:
with ROC = R, except for the possible addition or deletion of the origin or infinity.
n0 < 0,
Poles introduced at z=∞
4. Properties of z-Transform
One pole at z = a plus one 2nd-order pole at z = infinity

## Slide 68
3). Scaling in the z-domain:
with ROC = |z0| R.
|z0| R is a scaled version of R. It means if z is in the original ROC, R, then |z0|z is inside the new ROC.
4. Properties of z-Transform
Proof:
Note: the original poles are moved to |z0| zp , and the new ROC is determined by the new poles

## Slide 69
Example:
with ROC = R/2.
4. Properties of z-Transform
3). Scaling in the z-domain:
with ROC = |z0| R.

## Slide 70
Example:
with ROC = R/2.
For right-sided signal x[n],
rate with enlarged ROC.
3). Scaling in the z-domain:
with ROC = |z0| R.
helps for a faster decreasing
For left-sided signal x[n],
with smaller ROC.
gives a slower decreasing rate

## Slide 71
4). Time reversal:
with ROC = 1/R.
1/2
2
4. Properties of z-Transform
Proof:

## Slide 72
5). Time Expansion:
with ROC = R1/k.
4. Properties of z-Transform
k positive integer

## Slide 73
6). Conjugation:
with ROC = R.
Two steps: take conjugate of X(z) and replace z with z*
4. Properties of z-Transform
Proof:
Replace z with z*
ROC does NOT change.

## Slide 74
6). Conjugation:
with ROC = R.
Example:
Replace z with z*
From the property,

## Slide 75
6). Conjugation:
with ROC = R.
For real signal x[n], we have
For real signal x[n] with X(z) in rational form, the poles and zeros must come in conjugate pair.
4. Properties of z-Transform
Proof:
Similar proof for poles.

## Slide 76
Two poles:
6). Conjugation:
with ROC = R.

## Slide 77
Group discussion:
1. A real signal x[n] is known to have three poles for X(z). Two of them are at z = -2 and . It is also given
2. It is given that
The ROC of X(z) can be determined to be ( ).
It is known a stable LTI system has
The ROC of X(z) can be determined to be ( ).

## Slide 78
7). Convolution:
With ROC containing R1 ∩ R2.
Basis for LTI system analysis with ZT.
LTI
Different from DTFT, Y(z) is valid for the correct choice of ROC.
4. Properties of z-Transform

## Slide 79
7). Convolution:
With ROC containing R1 ∩ R2.

## Slide 80
Ex 10.15: Difference system
h[n] = ? The output when the input is unit impulse.
ROC:
On the other hand, do z-transform of both sides:
|z|>0
Basis for ZT analysis on LTI systems described by constant-coefficient difference equations.
4. Properties of z-Transform

## Slide 81
Ex 10.16: Accumulation
h[n] = ? The output when the input is unit impulse.
4. Properties of z-Transform
Note: Difference system and accumulation are reverse to each other

## Slide 82
8). Differentiation in the z-domain:
Example 10.17: From Example 10.14,
Can also obtain this result using differentiation in the z-domain.
4. Properties of z-Transform

## Slide 83
Example 10.17 (Cont’d):
Then, find the inverse z-transform for
With time shifting property,

## Slide 84
Example 10.18:
Do a differentiation in the z-domain,
A second-order pole at z=a.
4. Properties of z-Transform

## Slide 85
9). The Initial-Value Theorem
If x [n] = 0 for n < 0, then
Proof: If x [n] = 0 for n < 0,
4. Properties of z-Transform

## Slide 86
9). The Initial-Value Theorem
If x [n] = 0 for n < 0, then
Example 10.19:

## Slide 87
4. Properties of z-Transform
Table 10.2 for commonly-used z-transform pairs:
Why don’t we have z-transform for signals like
For x[n] = 1, we can write it as x[n] = u[n] + u[-n-1].
The intersection of the two ROC’s is empty.

## Slide 88
4. Properties of z-Transform
Summaries:
1. Understanding each property: how the time change affects both X(z) and its ROC;
2. Flexible usage of the properties:
Computing ZT, inverse ZT
Determine the ROC
LTI system analysis
……

## Slide 89
Partial fraction expansion for z-transform
First way:

## Slide 90
Partial fraction expansion for z-transform
Second way:
Try to do partial fraction expansion with 1/z instead of z. What happens if we do partial fraction expansion with z?

## Slide 91
Partial fraction expansion for z-transform
Third way:
Fourth way:

## Slide 92
Partial fraction expansion for z-transform

## Slide 93
Group discussion:
1. A causal signal X(z) has two poles at z=1/2, 1/3 and two zeros at z=0, z=1 plus x[0]=2. The signal is determined to be ( ).
2. Given that and a system The ROC for Y(z) of the output signal is ( ).

## Slide 94
5. Analysis of LTI systems using z-Transform
H(z)
LTI
Requirements:
Comprehensive understanding and application of knowledge about ZT.
Key is flexible usage of ZT and ROC properties.
Determine the input X(z) plus it ROC: …
Determine the system function H(z) and its ROC: …
Y(z) and its ROC, the inverse ZT for y[n]

## Slide 95
1). ROC from Causality property:
A). A discrete-time LTI system is causal if and only if the ROC of its system function is the exterior of a circle, including infinity.
From time-domain: h[n] = 0 for n < 0.
No matter whether the system function is in rational form or not.
5. Analysis of LTI systems using z-Transform

## Slide 96
1). ROC from Causality property:
B). A discrete-time LTI system with rational system function H(z) is causal if and only if:
a). The ROC is the exterior of a circle outside the outermost pole; and
b). With H(z) expressed as a ratio of polynomial in z, the order of the numerator cannot be greater than the order of the denominator.
Condition b) implies that after the expansion, no terms like z, z2, z3, etc. They refer to non-zero h[-1], h[-2], h[-3], etc. It is equivalent to ROC including ∞.
5. Analysis of LTI systems using z-Transform

## Slide 97
Example 10.20:
For this rational system function H(z), it is NOT causal since the order of the numerator is one order higher than the order of the denominator. Thus, after expansion, we will have a term like z, which refers to a nonzero h[-1].
5. Analysis of LTI systems using z-Transform
ROC for right-sided sequence?

## Slide 98
Example 10.21:
It is clearly causal. To confirm it with the above statement, we need to write H(z) as polynomial in z and compare the order of the numerator and the denominator.
The ROC is an outer ROC for both poles, so we can easily get the inverse z-transform as
5. Analysis of LTI systems using z-Transform

## Slide 99
2). ROC from Stability property:
A). An LTI system is stable if and only if the ROC of its system function H(z) includes the unit circle. (The DTFT then exists too.)
B). A causal LTI system with rational system function H(z) is stable if and only if all of the poles of H(z) lie inside the unit circle – i.e., they must all have magnitude smaller than 1.
5. Analysis of LTI systems using z-Transform

## Slide 100
Example 10.22:
Two poles: z = ½ and z = 2
5. Analysis of LTI systems using z-Transform
Poles and zeros plus possible ROC?
Three possible ROC.
Two zeros: z = 5/4 and z = 0
For each ROC, causal or stable?

## Slide 101
Example 10.22:
(1) |z| > 2, causal, unstable
Causal: an outside ROC including infinity.
Not stable: unit circle not included in the ROC.
Both terms are causal, but the second one is the reason for the system to be not stable.

## Slide 102
Example 10.22:
(2) ½ < |z| < 2, not-causal, stable
(3) |z| < ½ , anti-causal, not stable
Stable: unit circle included in the ROC.
Not causal: two-sided sequence

## Slide 103
Example 10.23: causal first-order system
5. Analysis of LTI systems using z-Transform
Stable:
Real system: a real number
Example 10.24: causal and real second-order system
Two conjugate poles:
Stable:

## Slide 104
Take z-transform of both sides,
Linear constant-coefficient difference equation:
Basis of ZT analysis on LTI system described by constant-coefficient difference equations.
5. Analysis of LTI systems using z-Transform

## Slide 105
However, no ROC can be derived from the difference equations. If at initial rest, then the system is causal and the ROC is outside the outermost pole.
Can be expressed in a rational form and can also be determined by its poles and zeros except for a constant factor.
5. Analysis of LTI systems using z-Transform

## Slide 106
Group discussion:
1. A rational system with only two poles at z = -1/2 and z = +2 plus the information that the output y[n]=0 when input x[n]=cos(πn). Determine which one of the following choice ( ) is true.
2. A system with real and causal h[n] and two poles for rational H(z) with one at z = (-1+j)/2. For system , determine which one of the following choice ( ) is true.
(a) Causal and stable
(b) Causal and not stable
(c) Not causal but stable
(d) Not causal and not stable
(a) Causal and stable
(b) Causal and not stable
(c) Not causal but stable
(d) Not causal and not stable

## Slide 107
Example 10.25:
Solution: take z-transform on both sizes
5. Analysis of LTI systems using z-Transform
One pole with two possible ROC’s
Causal and stable

## Slide 108
Example 10.25:
Solution (cont’d):
5. Analysis of LTI systems using z-Transform
Not causal and not stable
Question: why in the equation, only y[n-1], x[n-1] etc., no y[n+1], x[n+1]?
Causal requirement: y[n+1], x[n+1] refer to output and input signal for future time

## Slide 109
Example 10.26: Determine the system given
Solution: from the first piece of information,
5. Analysis of LTI systems using z-Transform

## Slide 110
Example 10.26 (Cont’d):
Using the convolution property:
ROC for H(z)?
Still two poles at:

## Slide 111
Example 10.26 (Cont’d):
Question: how to use the second information to find a?
(-1)n is a discrete-time complex exponential signal with zn and z = -1. Using system function, the output should be

## Slide 112
Example 10.26 (Cont’d):
To write out the difference equation, we have
Or,

## Slide 113
Example 10.27:
Consider a stable and causal system. Its H(z) is rational, contains a pole at z = ½ , and a zero somewhere on the unit circle. The locations of other poles and zeros are unknown.
For each of the following statements, determine whether it is true, or false, or can’t determine.
What do we know?
Stable, the ROC of H(z) includes the unit circle.
Rational and causal, an outside ROC.
One pole at z = ½ , ROC can NOT be inside |z| < ½ .

## Slide 114
Example 10.27 (Cont’d):
(1/2) R = R/2.
1
1/2
h(n)
1/2
(1/2)n h[n]
F{(1/2)n h[n]} converges.
Need to know whether the ROC of (1/2)n h[n] includes the unit circle.
What is the ROC of {(1/2)n h[n]:
Answer: True.
stable

## Slide 115
Example 10.27 (Cont’d):
We need to study the behavior of H(z) on the unit circle.
Answer: False. If it has finite duration, then the ROC should be the entire z-plane except the origin or infinity. However, H(z) has a pole at ½ .
(b) H(ejω) = 0 for some frequency.
(c) h[n] has finite duration.
Answer: True. Because there is a zero on the unit circle.

## Slide 116
Example 10.27 (Cont’d):
Answer: Can NOT determine. No sufficient information.
(d) h[n] is real.
For real signal with rational H(z), the poles and zeros must come in conjugate pairs or in real, but we only know that ½ is a real pole and we don’t know anything else about its poles and zeros.

## Slide 117
Example 10.27 (Cont’d):
For a stable system, the unit circle should be included in the ROC of G(z). What is the ROC of G(z)?
Answer: True. ROC still includes the unit circle.
(e) g[n] = n[h[n]*h[n]] is the impulse response of a stable system.

## Slide 118
Summaries:
Comprehensive understanding and application of knowledge about ZT.
1. Determine the input X(z) and its ROC
2. Determine the system function H(z) and its ROC: …
zeros, poles; difference equations;
given special input-output pair;
if x[n] = 1, y[n] = 0 … …
causal, stable; input-output pair;
3. Y(z) and its ROC, inverse ZT for y[n]
5. Analysis of LTI systems using z-Transform

## Slide 119
Group discussion:
1. For the following system under initial rest
(a) Causal and stable
(b) Causal and not stable
(c) Not causal but stable
(d) Not causal and not stable
Determine which one of the following choice ( ) is true.
(a) Causal and stable
(b) Causal and not stable
(c) Not causal but stable
(d) Not causal and not stable
2. For the following system with
Determine which one of the following choice ( ) is true for the system.

## Slide 120
6. System Function Algebra and Block Diagram
Basic requirements:
Can derive the system function from the system block diagram;
Several equivalent block diagrams are possible. Given a system function in rational form, can draw a block diagram, especially the direct-form.
Location of poles plus causal and stable properties
Inter-connection of sub-systems: will new poles be generated with new ROC?

## Slide 121
6. System Function Algebra and Block Diagram
Interconnections of LTI systems:
1) Determine the input and output of the system;
2) Decompose the system into subsystems, and find the input-output relationship for each subsystem;
3) Obtain the overall input-output relationship.

## Slide 122
6. System Function Algebra and Block Diagram
Series:
Parallel:
ROC? Causal or stable?
Convolution property and linear property: ROC no change
Plus, location of poles not change. Still outside ROC for causality and still ROC include the unit circle for stability

## Slide 123
Get rid of W(z), we have
6. System Function Algebra and Block Diagram
Feedback:
ROC? Causal or stable?
ROC: If the two subsystems are causal, the whole system will be causal. But, location of poles will change. ROC determined by new largest pole.

## Slide 124
Location of poles might change completely.
Feedback system
Unstable.
Examples: stable, causal
Stable.
A delayer:

## Slide 125
adder
Unit delay for difference
multiplication by a coefficient
Basic elements:
Examples 10.28 10.29 10.30 10.31
6. System Function Algebra and Block Diagram

## Slide 126
Examples 10.28：
6. System Function Algebra and Block Diagram

## Slide 127
Examples 10.28：
6. System Function Algebra and Block Diagram
Adder:
Note: No ROC is given here. The ROC is determined by new poles.

## Slide 128
Examples 10.29：
6. System Function Algebra and Block Diagram

## Slide 129
Examples 10.29：
Feedback
Feed-forward

## Slide 130
Examples 10.30：
6. System Function Algebra and Block Diagram
Feedback
ROC determined by poles

## Slide 131
Examples 10.31：
6. System Function Algebra and Block Diagram
Feedback
Feed-forward

## Slide 132
Examples 10.31：
6. System Function Algebra and Block Diagram

## Slide 133
Group discussion:
1. The following system function is for a causal system, its unit impulse response is ( )
2. Draw a system block diagram for the following system in direct form.

## Slide 134
7. Unilateral z-transform
Summation starts at n = 0.
Basic requirements:
Concept of UZ and its difference from bilateral ZT
Time-difference property of UZ and its application

## Slide 135
ROC: always an outside ROC.
If x[n] = 0 for n<0, then the unilateral z-transform of x[n] is the same as the bilateral z-transform of x[n]. Otherwise, the two might be different.
7. Unilateral z-transform

## Slide 136
Example 10.33: Find the bilateral and unilateral z-transform for
Bilateral z-transform:
Unilateral z-transform:

## Slide 137
Example 10.34: inverse z-transform
Bilateral z-transform: two poles with three possible ROC’s and one different signal for each ROC
Unilateral z-transform: only one possible ROC with the same inverse z-transform result as above

## Slide 138
7. Unilateral z-transform
Example 10.35:
Note: for unilateral z-transform, the degree of the numerator polynomial must be no bigger than the degree of the denominator.

## Slide 139
Properties: similar to the bilateral z-transform. Here, we focus on the differences.
Convolution: If x1[n] = x2 [n] = 0 for n<0, then
Time delay:
Time advance:
Why?
7. Unilateral z-transform

## Slide 140
Time delay:
Proof:
Note that for UZ of x[n-1], x[-1] is shifted into the range of the summation now.
7. Unilateral z-transform

## Slide 141
Time advance:
Proof:
Now, the summation starts at x[1], not x[0].
7. Unilateral z-transform

## Slide 142
For system at initial rest, the system is causal and thus H(z) is the same for the bilateral and unilateral z-transform.
The nice thing about unilateral z-transform is that it can be used to solve difference equations not at initial rest. (Now the system is NOT an LTI.)
Solving difference equations using unilateral z-transform:
7. Unilateral z-transform

## Slide 143
Under initial rest condition and
Example 10.36:
Solution:
7. Unilateral z-transform

## Slide 144
with
and
To find y[n], do unilateral z-transform of both sides:
Example 10.37:
Zero-state response
Zero-input response
Solution:

## Slide 145
with
and
Example 10.37:
Output at previous time, state
Solution:
In practice, to find the output

## Slide 146
1. Concept of z-transform: extension of DTFT to the complex domain
Commonly-used FT pairs:
LTI system:
Convergence: ROC determined by magnitude of z, pole-zero plot
Summary
If …,

## Slide 147
Summary
2. ROC properties:
3. Inverse ZT
(1) Four types of time-domain signals, four types of ROC
(2) ROC determined by poles, how to determine the ROC from possible ROC’s
Inverse LT based on partial fraction expansion
(3) Origin or infinity point removed from the ROC or not?
ROC outside the pole
ROC inside the pole

## Slide 148
Summary
4. Properties of ZT: be careful of ROC change

## Slide 149
Summary
6. System Function Algebra and Block Diagram
7. Unilateral z-transform
(1) Concept of unilateral ZT and difference from bilateral ZT
(2) Solving difference equations with non-zero initial conditions
(1) Series, parallel, feedback interconnection: ROC? Causal? Stable?
(2) Block diagram: system function
5. ZT-based system analysis
(1) Causal or stable property determined from ROC
(2) Systems of linear constant-coefficient difference equations
(3) Flexible usage of ZT properties

## Slide 150
Group discussion:
1. The unilateral ZT for signal is ( )
2. Which signals ( ) have the following unilateral ZT ?