## Slide 1
Ch.4 The Continuous-Time Fourier Transform
Representation of Aperiodic Signals: Continuous-Time Fourier Transform (Ch.4.1)
FT for Periodic Signals (Ch.4.2)
Properties of Continuous-Time FT (Ch.4.3)
The Convolution Property (Ch.4.4)
The Multiplication Property (Ch.4.5)
Tables of Fourier Transform Properties and of Basic FT Pairs (Ch.4.6)
Systems Characterized by Linear Constant-Coefficient Differential Equations (Ch.4.7)

## Slide 2
Frequency domain analysis: periodic in time
LTI system unit impulse response: h(t), aperiodic in time
How about frequency domain analysis for signals aperiodic in time?

## Slide 3
T = 4T1
T = 8T1
T = 16T1
the same frequency
Fix pulse shape, increase period
the same envelope in frequency

## Slide 4
As T increases, we have two observations:
The harmonics are packed more and more closer to each other;
However, the shape (the envelope) of the spectrum remains the same (and it is determined by the pulse shape of the signal).
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
1). Development of the Fourier transform representation of an aperiodic signal
( Go from Fourier series to Fourier transform )

## Slide 5
(2) Go from periodic to aperiodic
Construct a periodic signal from the aperiodic signal x(t); later, let
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
No overlap in time

## Slide 6
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
For periodic signal , we have its Fourier series:
For aperiodic signal x(t) :
How to find a similar expression for the aperiodic signal?

## Slide 7
Define
then
Decompose the signal into combinations of exponentials
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform

## Slide 8
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
Fourier transform:
or
The signal as a combination of complex exponentials, the same as FS with harmonics.
Either time-domain or frequency-domain and they are equivalent.
A signal has a unique spectrum and a spectrum is for a unique signal.

## Slide 9
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
About LTI system:
Unit impulse response:
System frequency response:
Either the time-domain or frequency-domain description can be used.

## Slide 10
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
Connection between the periodic and aperiodic signals:

## Slide 11
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
2). Convergence of Fourier transform
(3) x(t) has a finite number of discontinuity within any finite interval. Furthermore, each of these discontinuities must be finite.
(1) x(t) is absolutely integrable.
(2) x(t) has a finite number of maxima and minima within any finite interval.
Dirichlet conditions:
Note: if an LTI system has frequency response,
A stable system

## Slide 12
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
Example (1):
Prove: Use
Note: from FS, a signal like has only one frequency component. Its FT is an impulse in the frequency.

## Slide 13
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
Example (2):
Note: cos( ) and sin( ) are composed of the same two frequency components. Different phases generate signals of different form.

## Slide 14
Group discussion:
1. If a signal is used as the input to LTI systems, which of the following outputs can be generated:
2. If a signal is used as the input to an causal LTI systems, which of the following outputs can be generated:

## Slide 15
Example 4.1:
Solution:
Find Fourier transform of
while the other is oscillating and bounded
Complex function.
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
The signal is absolutely integrable.

## Slide 16
Example 4.1 (Cont’d):
0
0
0
Magnitude spectrum
Phase spectrum

## Slide 17
Example 4.1 (Cont’d):
A complex spectrum, but for real signal x(t)
Conjugate:
Frequency reversal:
Conjugate and frequency reversal:

## Slide 18
Example 4.2:
Solution:
Find FT of
Note: this signal is real in time and has a real spectrum
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform

## Slide 19
Example 4.3:
Solution:
Find Fourier transform of
Note that this signal does not meet the Dirichlet condition 3, finite discontinuity. However, it is a very important signal.
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
Note: in order to support the impulse behavior for the signal, it must have all frequency components included.

## Slide 20
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
Example 4.4:
Solution:
Fourier transform of aperiodic square-wave
Real signal and real spectrum
First zero-crossing frequency

## Slide 21
Example 4.4 (Cont’d):
2. A perfect square-wave in time has a sharp transition in time-domain with an oscillating spectrum in the frequency-domain.
Example 4.5:
How about a perfect square-spectrum in the frequency-domain?
Note:
1. A perfect square-wave in time has infinite frequency components;

## Slide 22
Example 4.5:
A perfect square spectrum
Solution:
Let
then

## Slide 23
Example 4.5:
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
Note: the wider the bandwidth, the narrower the pulse in time
the narrower the bandwidth, the wider the pulse in time

## Slide 24
Example 4.5:
Solution:
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
Note: A perfect ideal lowpass filter, but bad time-domain properties like non-causal, oscillation in time, low convergence rate
How to deal with these problems in practice:
cutoff in time, plus time delay for causality

## Slide 25
Example 4.5:
1. Representation of Aperiodic Signals: Continuous-Time Fourier Transform
cutoff in time

## Slide 26
2. Fourier Transform for Periodic Signals (Ch.4.2)
Periodic signal:
thus
Especially,

## Slide 27
Example 4.7:
Another solution:
is a periodic signal with FS
Others are 0.
2. Fourier Transform for Periodic Signals (Ch.4.2)

## Slide 28
Example 4.8:
Solution: Example 3.8
An impulse train
…
…
0
T
-T
2. Fourier Transform for Periodic Signals (Ch.4.2)
1

## Slide 29
Example 4.8 (Cont’d):
An impulse train in the time-domain gives an impulse train in the frequency-domain.
…
…
0

## Slide 30
Group discussion:
1. For the following LTI system with
Find the output signal when the input signal is

## Slide 31
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
Note: the same underlying principles behind FT and FS
plus, similar operations for both FT and FS, and thus similar properties for FT and FS.

## Slide 32
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
then
If
1). Linearity:
For both periodic and aperiodic signals.
Example:
Solution: Aperiodic signal, no FS, but
Find the Fourier Transform for

## Slide 33
2). Time Shifting:
Proof:
The same spectrum except for a linear phase.
Let
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)

## Slide 34
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
2). Time Shifting:
Another proof:
First
then
Note: similar to FS, two different ways to prove the FT properties

## Slide 35
Example 4.9:
Find the Fourier transform of
1
4
1
3
2
1.5
=
1
4
1
3
2
4
1
3
2
0.5
+
+
Square-wave
and time shift of 2.5
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)

## Slide 36
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
3). Conjugation and Conjugate Symmetry:
then
(1) If
and
(2) If x(t) is real, then

## Slide 37
Proof:
Not a standard synthesis equation
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)

## Slide 38
also write
(3) If x(t) is real, and write
Then,
For example:
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
For a real and even signal, its Fourier transform will be real; for a real and odd signal, its Fourier transform will be purely imaginary.

## Slide 39
4). Differentiation and Integration:
, then
(1) If
then
(2) If
Proof:
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)

## Slide 40
Example 4.12:
x(t)
1
-1
1
-1
Find X( jω).
Here, we first find . What do you get?
g(t) =
1
1
-1
-1
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)

## Slide 41
Example 4.12 (Cont’d):
Black part: a square-wave
Red part: two unit impulses
with
g(t) =
1
1
-1
-1

## Slide 42
Example 4.12 (Cont’d):
with
g(t) =
1
1
-1
-1

## Slide 43
5). Time and Frequency Scaling:
Especially, for time reversal,
Proof:
a>0
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)

## Slide 44
5). Time and Frequency Scaling:
Proof:
a<0
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
Especially, for time reversal,

## Slide 45
5). Time and Frequency Scaling:
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
Time compression
Frequency expansion
Time expansion
Frequency compression
Note: time compression, same waveform variation within shorter time, thus higher frequency components to support

## Slide 46
Group discussion:
1. Given that , which one of the following is the correct FT for the signal
2. Given that , which one of the following is the correct signal for

## Slide 47
6). Duality:
Proof:
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)

## Slide 48
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)

## Slide 49
Find the FT of
Example 4.13:
By Duality,
From example 4.2,
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)

## Slide 50
6). Duality: other important results from duality
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
Aperiodic signal, any frequency shifting
Periodic signal, only multiples of harmonic frequency

## Slide 51
7). Parseval’s Relation:
Proof:
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
Aperiodic signal’s energy

## Slide 52
7). Parseval’s Relation:
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
Periodic signal, FS

## Slide 53
Example 4.14: Evaluate the following:
for the two following signal spectrum
-1
- 0.5
0.5
1
(a)
-1
1
(b)
3. Properties of Continuous-Time Fourier Transform (Ch.4.3)
Note: the spectrum is given, the signal is known. determine the signal in time first?

## Slide 54
-1
- 0.5
0.5
1
(a)
-1
1
(b)
Solution:
(a)
(b)
Example 4.14 (Cont’d):

## Slide 55
Note that
(a)
is odd.
D = 0 since
(b)
Let
then
Example 4.14 (Cont’d):
-1
- 0.5
0.5
1
(a)
-1
1
(b)

## Slide 56
Group discussion:
1. Compute the following integral
Which one of the choice is the correct result?

## Slide 57
4. The Convolution Property (Ch.4.4)
h(t)
H(j)
x(t)
y(t)=x(t)*h(t)
X(j )
Y(j)=X(j)H(j)
Consider an LTI system:
Since h(t) completely characterize an LTI system, so does H( j). And H( j) exists if h(t) satisfies the Dirichlet conditions.

## Slide 58
4. The Convolution Property (Ch.4.4)

## Slide 59
Proof 1:
A linear combination of frequency components as complex exponentials and an LTI system, with
4. The Convolution Property (Ch.4.4)

## Slide 60
Proof 2:
4. The Convolution Property (Ch.4.4)

## Slide 61
Example 4.15:
A system with
A simple LTI system.
To find its unit impulse response:
with time-shifting property
From
4. The Convolution Property (Ch.4.4)

## Slide 62
Example 4.16:
An LTI system defined as
Find the frequency response of the system.
4. The Convolution Property (Ch.4.4)

## Slide 63
Example 4.17:
--- integration
Note:
4. The Convolution Property (Ch.4.4)

## Slide 64
Example 4.18:
a perfect low-pass filter
Perfect frequency characteristics, but in time:
1. not causal
2. oscillating in time may not be desirable.
Reason: sharp transition in frequency
passband
stopband
Why?
4. The Convolution Property (Ch.4.4)

## Slide 65
Example 4.19:
An LTI system defined as
with an input
Find its output.
Solution:
Convolution in time for

## Slide 66
Example 4.19:
if
Solution:
Frequency multiplication,
Then, do inverse Fourier transform,
The key is how to do the expansion.

## Slide 67
If b = a,
Example 4.19 (Cont’d):
Time convolution,

## Slide 68
In general,
See Problem Exercise 4.40
Example 4.20:
Please read the textbook yourself.
Example 4.19 (Cont’d):

## Slide 69
Group discussion:
1. Compute the following integral

## Slide 70
Partial Fraction Expansion (Appendix)
Example:
Then use
for each term.
To find the inverse Fourier transform of
expand Y(jω) as

## Slide 71
--- a ratio of polynomial
In general,
Question:
How to expand H(v) as a sum of terms like
For Fourier transform, replace v with jω.
Partial Fraction Expansion (Appendix)

## Slide 72
1. If
, use polynomial division, we have
……
For Fourier transform,
Partial Fraction Expansion (Appendix)

## Slide 73
2. proper rational function
Example:
Partial Fraction Expansion (Appendix)

## Slide 74
Example:
1). If the three roots are not equal, that is p1 ≠ p2≠ p3 ,
Suppose p1 , p2 , p3 are the roots of
then
How to find A1 , A2 , A3 ?
Partial Fraction Expansion (Appendix)

## Slide 75
for any v.
Partial Fraction Expansion (Appendix)

## Slide 76
Another way to find the coefficients:
Note
Partial Fraction Expansion (Appendix)

## Slide 77
2). If p1 = p3≠ p2 ,
both terms are necessary!
Partial Fraction Expansion (Appendix)

## Slide 78
Partial Fraction Expansion (Appendix)
In-correct!

## Slide 79
with
Partial Fraction Expansion (Appendix)

## Slide 80
Partial Fraction Expansion (Appendix)
Example:

## Slide 81
Partial Fraction Expansion (Appendix)
Example:

## Slide 82
Partial Fraction Expansion (Appendix)
Example:
To find :

## Slide 83
Group discussion:
1. Do polynomial division on
The result of G(v) is which one of the following choices.
2. Do partial fraction expansion to get the parameter A and B.

## Slide 84
5. The Multiplication Property (Ch.4.5)
The multiplication (modulation) property:
s(t)
p(t)
r(t)
Duality property of Fourier transform
Non-LTI system

## Slide 85
5. The Multiplication Property (Ch.4.5)
Proof: similar to convolution property

## Slide 86
Proof:

## Slide 87
5. The Multiplication Property (Ch.4.5)
Othogonality between complex exponential signals:
Harmonics:
In a general form:
Signals orthogonal to each other can be used as different dimensions for signal representation in general.

## Slide 88
Example 4.21:
Find the spectrum for r(t) with
Solution with multiplication property:
5. The Multiplication Property (Ch.4.5)

## Slide 89
Two copies of the original signal shifted to different frequencies.
5. The Multiplication Property (Ch.4.5)

## Slide 90
Another solution：
Frequency shifting property:
5. The Multiplication Property (Ch.4.5)
Note: seen as a system with input s(t) and output r(t). New frequency components different from the input are generated at the output, thus, the system is not an LTI system

## Slide 91
Example 4.22:
Note: should shift the whole spectrum.
5. The Multiplication Property (Ch.4.5)

## Slide 92
Recovering the original signal using a low-pass filter if no spectrum overlapping with large enough ω0.
Example 4.22 (Cont’d):

## Slide 93
Another solution:
Example 4.22 (Cont’d):

## Slide 94
Example 4.23:
find its FT.
Solution: analysis equation? No way
Transform x(t) into some signals you know
5. The Multiplication Property (Ch.4.5)

## Slide 95
Example 4.23 (Cont’d):
Note: an important example for FT computation with sinc() signals

## Slide 96
Frequency-Selective Filtering with Variable Center Frequency
A Bandpass Filter :
5. The Multiplication Property (Ch.4.5)

## Slide 97
Equivalent to
5. The Multiplication Property (Ch.4.5)

## Slide 98
Group discussion:
1. Prove the orthogonal property between the two signals:
2. Compute the following integral given the signal’s spectrum.
1
1
-1
The result is which one of the following choices.

## Slide 99
6. Tables of Fourier Properties and of Basic Fourier Transform Pairs (Ch.4.6)
Table 4.1
Table 4.2

## Slide 100
7. Systems Characterized by Linear Constant-Coefficient Differential Equations (Ch.4.7)
If true, take Fourier transform:
Frequency response
Time-domain description:
A casual LTI system if under initial rest.
Unit impulse response

## Slide 101
Causal system and if a > 0, the system is stable.
Example 4.24:
Fourier transform:
7. Systems Characterized by Linear Constant-Coefficient Differential Equations (Ch.4.7)

## Slide 102
Example 4.25:
7. Systems Characterized by Linear Constant-Coefficient Differential Equations (Ch.4.7)

## Slide 103
Example 4.26:
The system from Example 4.25 with input
Example 4.25 (Cont’d):
Causal and stable system.
Find the output signal in time.

## Slide 104
Example 4.26:
7. Systems Characterized by Linear Constant-Coefficient Differential Equations (Ch.4.7)

## Slide 105
Example 4.26 (Cont’d):
Take

## Slide 106
Example 4.26 (Cont’d):

## Slide 107
Group discussion:
1. For the following system described by
under initial rest. Try to find the unit impulse response h(t) of the system.
2. Do partial fraction expansion to get the parameters A, B and C.

## Slide 108
Extra Example 1:
In this textbook, no rigorous proof on this FT pair. Instead,
To get this FT pair, assume the time integral property is known:
To prove the time integral property, assume the FT pair is known:
Any other possible way to prove this important FT pair?

## Slide 109
Extra Example 1:
Real and odd signal, purely imaginary spectrum
No matter how small ω is!

## Slide 110
Extra Example 1:
Why incorrect?
For any non-zero a

## Slide 111
Extra Example 2: Hilbert transform
Duality:
90-degree phase shifter
Any frequency components passing through this system will have its magnitude unchanged, but a 90-degree phase shifting.

## Slide 112
Extra Example 3: Circuit analysis using FT
Impedance:
Input
Output

## Slide 113
Point A:
Point B:
An ideal amplifier:
Given the three equations, the three unknown voltage can be solved.

## Slide 114
Extra Example 3: Circuit analysis using FT
3dB bandwidth:
Given that
Frequency response:
Unit impulse response:

## Slide 115
Extra Example 4: properties of
2. Example 4.23, Compute the FT of
3. Prove
4. Compute the following integral given the signal’s spectrum.
1
1
-1
An ideal low-pass filter type spectrum
1. Frequency-selective filtering:

## Slide 116
Other Examples:
1. Poisson formula: let
2. Compute

## Slide 117
Group discussion:
1. Assume that , find
2. Let , prove that
The result is which one of the following choices.

## Slide 118
1. Continuous-Time Fourier Transform of Aperiodic Signals
Summary
Commonly-used FT pairs
LTI system:
A stable system
Convergence:

## Slide 119
Summary
2. Continuous-Time Fourier Transform of Periodic Signals
3. Properties of Continuous-Time Fourier transform

## Slide 120
Summary
4. The Convolution Property:
5. The Multiplication Property:
Partial fraction expansion
6. Systems Characterized by Linear Constant-Coefficient Differential Equations: frequency analysis