## Slide 1
Ch.9 The Laplace Transform
1. The Laplace Transform (Ch.9.1)
2. The Region of Convergence for Laplace Transform (Ch.9.2)
3. The Inverse Laplace Transform (Ch.9.3)
4. Properties of Laplace Transform (Ch.9.5)
5. Analysis of LTI systems using LT (Ch.9.7)
6. System Function Algebra and Block Diagram
7. Unilateral Laplace Transform (Ch.9.9)

## Slide 2
1. The Laplace Transform (Ch.9.1)
Why do we need Laplace transform?
1. A generalization of Fourier transform.
2. A signal or system may not have Fourier transform. (Dirichlet conditions)
3. Laplace transform allows easy study on stability or causality of a system.

## Slide 3
Review from Chapter 3 (Fourier series)
h(t)
x(t)=est
y(t)=H(s)est
--- Laplace transform of h(t).
System function
if converging on the jω-axis.
Connection with FT, or the frequency response:
1. The Laplace Transform (Ch.9.1)
For any complex number with converging integral

## Slide 4
Basic requirements:
1. Definition of Laplace transform
2. Concept of ROC (Region of Convergence)
3. Commonly-used LT pairs
4. How to find the LT of a signal
5. Concept of zeros and poles
1. The Laplace Transform (Ch.9.1)

## Slide 5
(1) Definition
(2) Definition based on Fourier transform
Fourier transform of with suitable  for the integral to converge.
1. The Laplace Transform (Ch.9.1)
Note: The ROC is only determined by Re{s}= .

## Slide 6
Re
Re
S-plane
S-plane
Im
Im
-a
-a
(3) Region of Convergence ( ROC )
ROC: Range of  for X(s) to converge
Representation: A. Inequality
B. Region in S-plane
The ROC is determined by Re{s}=  and it consists of strips parallel to jω-axis.
1. The Laplace Transform (Ch.9.1)

## Slide 7
(4) Relationship between Fourier and Laplace transform
Example 9.1 9.2 9.3 9.4 9.5
if the ROC includes the jω-axis.
1. The Laplace Transform (Ch.9.1)
Note: the same LT expression, but different ROC’s. Only one of them has FT transform

## Slide 8
Ex 9.1:
Fourier transform:
b) When a < 0, x(t) is exponentially increasing in the positive time and its Fourier transform does NOT exist
How about the Laplace transform for x(t)?
a) When a > 0, x(t) is exponentially decreasing in the positive time and its Fourier transform exists
1. The Laplace Transform (Ch.9.1)
with positive a

## Slide 9
Ex 9.1: Find the Laplace transform of
Solution:
Bounded

## Slide 10
or
Ex 9.1: Find the Laplace transform of

## Slide 11
Note the following:
1. The ROC consists of strips parallel to the jω-axis.
2. If a > 0, x(t) is absolutely integrable and has Fourier transform; also, the ROC for X(s) includes the jω-axis.
If the Fourier transform exists, then
Ex 9.1: Find the Laplace transform of

## Slide 12
Ex 9.2: Find the Laplace transform of
Solution:
To make exponentially decreasing in negative time.
1. The Laplace Transform (Ch.9.1)

## Slide 13
Ex 9.2: Find the Laplace transform of

## Slide 14
Important results:
ROC is important and never forget to write down the ROC for a Laplace transform.
Expression plus ROC determines the Laplace transform for a signal.
1. The Laplace Transform (Ch.9.1)
Right-sided
Left-sided
Right-sided
Left-sided

## Slide 15
Group discussion:
1. Given an LTI system with , determine the possible output signal if the input signal is
2. Given an LTI system with , determine the possible output signal if the input signal is

## Slide 16
Ex 9.3:
Solution:
Laplace transform is linear.
Laplace transform in rational form
The ROC is the overlap of the two.
1. The Laplace Transform (Ch.9.1)
Note: The ROC is determined by the roots of the denominator.

## Slide 17
Ex 9.4:
Solution:
Laplace transform in rational form
1. The Laplace Transform (Ch.9.1)

## Slide 18
Ex 9.5:
Solution:
for any s.
Its ROC is the entire s-plane.
1. The Laplace Transform (Ch.9.1)

## Slide 19
Note that: some signals do not have LT
The two ROC don’t overlap.
Time-domain:
s-domain:
1. The Laplace Transform (Ch.9.1)

## Slide 20
Note that: some signals do not have LT
The two ROC don’t overlap.
s-domain:
1. The Laplace Transform (Ch.9.1)
Divergent on the jω-axis.
Another example:
However,

## Slide 21
Laplace transform in rational form
Pole-zero plot:
zeros --- roots of the numerator polynomial and X(s) = 0; (if outside ROC, X(s) = infinity)
poles --- roots of the denominator polynomial and X(s) = infinity; ROC can not contain poles. Why?
Poles and zeroes can be defined for both Laplace transform of rational form and LT of irrational form.
1. The Laplace Transform (Ch.9.1)

## Slide 22
In general,
1. If the order of the denominator exceeds the order of the numerator by k, then X(s) will have k zeros at infinity
2. If the order of the numerator exceeds the order of the denominator by k, then X(s) will have k poles at infinity.
Note that there might exist poles or zeros at infinity. For example, 1/s has a pole at s=0 and a zero at s=infinity.
1. The Laplace Transform (Ch.9.1)

## Slide 23
Pole-zero plot:
Example 9.5:
No Fourier transform for this signal. Why?
The ROC can NOT contain poles.
1. The Laplace Transform (Ch.9.1)
Note: For the zero outside ROC, can confirm that

## Slide 24
Summaries:
1. Definition of Laplace transform and its connection with FT, system function
2. Concept of ROC and its importance
3. Commonly-used LT pairs
4. How to find the
LT of a signal
Linear property of LT, ROC intersection
5. LT in rational form
6. Concept of zeros and poles: no poles in the ROC
1. The Laplace Transform (Ch.9.1)

## Slide 25
Exercise 9.44:
1. The Laplace Transform (Ch.9.1)
ROC:
Still a right-sided signal with right-sided ROC

## Slide 26
Exercise 9.44:
1. The Laplace Transform (Ch.9.1)
Note: Another example, see Exercise 9.60
poles:
But complex numbers:
Re
Im
-1

## Slide 27
Group discussion:
1. For the signal , its Laplace transform has ( ) number of zeros in the finite s-plane.
2. From the ROC of the signal’s x(t) = u(t) Laplace transform, does the signal u(t) have Fourier transform or not?

## Slide 28
2. The Region of Convergence for Laplace Transform (Ch.9.2)
For Fourier transform, we have Dirichlet conditions for its convergence; here, we need to study the ROC.
Basic requirements:
1. Based on the properties of ROC, can determine the ROC of a signal’s LT from its time-domain property (four types of signals).
2. Understanding and flexible usage of the properties

## Slide 29
Property 1: The ROC of X(s) consists of strips parallel to j-axis in the s-plane. (The ROC is determined by Re{s}.)
Property 2: For rational Laplace transform, the ROC does not contain any poles. (At the pole, X(s) = infinity. )
2. The Region of Convergence for Laplace Transform (Ch.9.2)

## Slide 30
Property 3: If x(t) is of finite duration and is absolutely integrable, then the ROC is the entire s-plane.
(1). σ> 0, the exponential is monotonically decreasing,
2. The Region of Convergence for Laplace Transform (Ch.9.2)
Proof: absolutely integrable

## Slide 31
Property 3: If x(t) is of finite duration and is absolutely integrable, then the ROC is the entire s-plane.
Proof (cont’d):
(2). σ< 0, the exponential is monotonically increasing,
2. The Region of Convergence for Laplace Transform (Ch.9.2)
In summary, no matter what σ (positive or negative) is, the integral X(s) is converging and the ROC is the entire s-plane.

## Slide 32
Example 9.6:
Otherwise, x(t) = 0.
Looks like X(s) has a pole at s = -a. While from Property (3), the ROC should be the entire s-plane. Which one is correct?
Solution:
2. The Region of Convergence for Laplace Transform (Ch.9.2)

## Slide 33
Example 9.6:
Otherwise, x(t) = 0.
The ROC is the entire s-plane.
2. The Region of Convergence for Laplace Transform (Ch.9.2)
No poles on the finite s-plane.
Zeros:
Re
Im
Many zeros equally spaced on the Im-axis

## Slide 34
Property 4: If x(t) is right sided, and if the line Re{s}=0 is in the ROC, then all values of s for which Re{s}>0 will also be in the ROC.
σ0
0
σ
jω
However, not necessarily the boundary for the ROC!
2. The Region of Convergence for Laplace Transform (Ch.9.2)

## Slide 35
x(t)
T2
t
e-0t
e-1t
Property 5: If x(t) is left sided, and if the line Re{s}=0 is in the ROC, then all values of s for which Re{s}<0 will also be in the ROC.
σ0
0
σ
jω
However, not necessarily the boundary!
2. The Region of Convergence for Laplace Transform (Ch.9.2)

## Slide 36
Property 6: If x(t) is two sided, and if the line Re{s}=0 is in the ROC, then the ROC will consist of a strip in the s-plane that includes the line Re{s}=0 .
σ0
σ
Don’t know where the boundary is!
2. The Region of Convergence for Laplace Transform (Ch.9.2)

## Slide 37
S-plane
Re
Re
Re
Im
Im
Im
R
L
L
R
The three different cases:
Example 9.7:
The key is to divide the signal into one right sided signal and one left sided signal.
2. The Region of Convergence for Laplace Transform (Ch.9.2)

## Slide 38
Property 7: If the Laplace transform X(s) of x(t) is rational, then its ROC is bounded by poles or extends to infinity. In addition, no poles of X(s) are contained in the ROC.
Property 8: If the Laplace transform X(s) of x(t) is rational, then if x(t) is right sided, the ROC is the region in the s-plane to the right of the rightmost pole. If x(t) is left sided, the ROC is the region in the s-plane to the left of the leftmost pole. (Here, we do NOT include poles at infinity.)
2. The Region of Convergence for Laplace Transform (Ch.9.2)

## Slide 39
Example 9.8:
Two poles at
s = -1 and s = -2.
0
Three possible ROC’s:
-1
-2
0
-1
-2
0
-1
-2
Re{s} > -1
Re{s} < -2
-2 <Re{s}<-1
Each one of them corresponds to a different signal.
2. The Region of Convergence for Laplace Transform (Ch.9.2)

## Slide 40
Summaries:
1. ROC: strips parallel to the imaginary axis in the s-plane
2. Four different types of signals, corresponds to four different types of ROC
3. For rational LT, ROC is bounded by poles: rightmost pole and the leftmost pole
2. The Region of Convergence for Laplace Transform (Ch.9.2)
Note: No non-contiguous ROC. For example, three poles, -2, -1, and +1, no following ROC:
-2 < Re{s} < -1 OR Re{s} > +1

## Slide 41
Group discussion:
1. For the signal , the ROC of its Laplace transform is ( )
2. For the following and an absolutely integrable signal, the signal is ( )

## Slide 42
3. The Inverse Laplace Transform (Ch.9.3)
Basic requirements:
Understanding the concept of inverse LT: a contour integral in the ROC;
Inverse LT based on partial fraction expansion

## Slide 43
Contour integral in the ROC of the complex s-plane. The contour is a straight line parallel to the imaginary axis.
3. The Inverse Laplace Transform (Ch.9.3)
Write X(s) as a FT with suitable chosen real part:
Based on the one-to-one mapping property of FT:
Finally:

## Slide 44
The calculation for inverse Laplace transform:
(1) Contour Integration of complex function.
(2) Compute by partial fraction expansion.
Important transform pair:
Example 9.9 9.10 9.11
3. The Inverse Laplace Transform (Ch.9.3)

## Slide 45
1. Determine the ROC of the LT: poles and other conditions;
2. Partial fraction expansion of the LT;
3. For each term, do the inverse LT with the determined ROC based on
For example:
3. The Inverse Laplace Transform (Ch.9.3)

## Slide 46
The two poles at s = -1 and -2 give three possible ROC’s.
0
-1
-2
0
-1
-2
0
-1
-2
Re{s} > -1
Re{s} < -2
-2 <Re{s}<-1
3. The Inverse Laplace Transform (Ch.9.3)

## Slide 47
Do partial fraction expansion (independent of ROC):
3. The Inverse Laplace Transform (Ch.9.3)

## Slide 48
(1). Re{s} > -1:
Inverse LT for each term
a right ROC to the pole
a right-sided signal
0
-1
-2
3. The Inverse Laplace Transform (Ch.9.3)

## Slide 49
(2). Re{s} < -2: The same partial fraction expansion
For both terms, the ROC is a left ROC to the pole
3. The Inverse Laplace Transform (Ch.9.3)

## Slide 50
(3). -2 < Re{s} < -1:
For the first term, the ROC is a left ROC to the pole
For the second term, the ROC is a right ROC to the pole
0
-1
-2
3. The Inverse Laplace Transform (Ch.9.3)

## Slide 51
1. Determine the ROC of the LT: poles and other conditions;
2. Partial fraction expansion of the LT;
3. For each term, do the inverse LT with the determined ROC based on
Summaries:
3. The Inverse Laplace Transform (Ch.9.3)

## Slide 52
Extra examples:
1. Given , and x(t) is
absolutely integrable, determine x(t).
2. Given , and
determine x(t).
3. The Inverse Laplace Transform (Ch.9.3)
ROC includes the Im-aixs.
ROC includes Re{s}=0 line.

## Slide 53
Extra. Geometric evaluation of FT (Ch.9.4)
Example:
Re
Im

## Slide 54
Extra. Geometric evaluation of FT (Ch.9.4)
First-order system:
Re
Im
Low-pass type:

## Slide 55
Extra. Geometric evaluation of FT (Ch.9.4)
All-pass system:
Re
Im
Second-order system:

## Slide 56
Extra. Geometric evaluation of FT (Ch.9.4)
High-pass system:
Band-pass system:

## Slide 57
Group discussion:
1. Do partial fraction on , the result is ( )
2. Do the inverse LT for the previous signal if the signal has FT.

## Slide 58
4. Properties of Laplace Transform (Ch. 9.5)
Basic requirements:
1. Understanding each property: how the time transform affects both X(s) and its ROC;
2. Flexible usage of the properties:
Computing LT, inverse LT
Determine the ROC
LTI system analysis
……

## Slide 59
1). Linearity
Note that the ROC of x(t) is at least the intersection of R1 and R2. It could be empty, and it could be larger than the intersection.
Why?
Change in the ROC is also important.
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 60
Example 9.13:
Now,
This is called pole-zero cancellation.
Since we have only one pole now at s = -2, we can extend the original ROC to Re{s} > -2 .
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 61
1). Linearity
Only true for sum of finite terms!
4. Properties of Laplace Transform (Ch. 9.5)
Exercise 9.44:
A right-sided impulse train
A right-sided ROC

## Slide 62
2). Time shifting:
with ROC = R.
A time shift doesn’t affect the convergence.
Proof: (The same as in the Fourier transform.)
4. Properties of Laplace Transform (Ch. 9.5)
No change on the exponential varying rate, no change on poles.

## Slide 63
3). Shifting in the s-domain:
Meaning?
For any s in the original ROC R, s + Re{s0} will be in the new ROC. (Or, shift the ROC by Re{s0}.)
with ROC = R + Re{s0}.
4. Properties of Laplace Transform (Ch. 9.5)
Meanwhile, from the property:

## Slide 64
3). Shifting in the s-domain:
Given , and
has FT, determine x(t).
Example:
4. Properties of Laplace Transform (Ch. 9.5)
Note: the change on ROC can also be treated as change on poles, but the direction of the ROC remains, for example, still right-sided signal with right-sided ROC
Meaning?
For any s in the original ROC R, s + Re{s0} will be in the new ROC. (Or, shift the ROC by Re{s0}.)
with ROC = R + Re{s0}.

## Slide 65
3). Shifting in the s-domain:
has FT, determine x(t).
4. Properties of Laplace Transform (Ch. 9.5)
with ROC = R + Re{s0}.
Example: given that , and
Solution: the key is to determine the ROC for X(s). Two poles with three possible ROC as
Due to the fact that the new signal has FT, thus

## Slide 66
4). Time scaling:
with ROC = aR.
Proof:
with ROC = -R.
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 67
5). Conjugation:
with ROC = R.
take conjugate of X(s) and replace s with s*.
Proof:
First, take conjugate of the function:
Then, replace s with s*:
The ROC does NOT change, why?
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 68
5). Conjugation:
with ROC = R.
Example:
While, from the property:
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 69
5). Conjugation:
If x(t) is real,
and its zeros and poles must come in conjugate pairs.
For example, if x(t) is real and s = -1+j is a pole, then s = -1-j must also be a pole.
Proof: if
then
Thus, also a zero for X(s).
4. Properties of Laplace Transform (Ch. 9.5)
Similar proof for poles.

## Slide 70
6). Convolution:
Proof?
Basis for LTI system analysis with LT.
LTI
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 71
6). Convolution:
LTI
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 72
Group discussion:
1. A real signal x(t) is known to have three poles for X(s). Two of them are at s = -2 and s = +1+2j. It is also given
2. It is given that
The ROC of X(s) can be determined to be ( ).
It is known a stable LTI system has
The ROC of X(s) can be determined to be ( ).

## Slide 73
7). Differentiation in the Time-Domain:
Basis for LT analysis on LTI systems described by constant-coefficient differential equations.
For example:
4. Properties of Laplace Transform (Ch. 9.5)
Example:

## Slide 74
8). Differentiation in the s-domain:
How to explain that the signal has its ROC not changed?
1. From time domain, tx(t) will not change the exponential varying rate of the signal in time
4. Properties of Laplace Transform (Ch. 9.5)
2. From complex domain, will not change the location of poles

## Slide 75
8). Differentiation in the s-domain:
Example 9.14:
Use the property:
In general:
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 76
Example 9.15: Do the inverse Laplace transform for
Do partial fraction expansion:
Solution:

## Slide 77
Example 9.15: Do the inverse Laplace transform for
Solution:

## Slide 78
9). Integration in the time-domain:
with ROC containing R Ո {Re{s}>0}.
Proof:
Also note that,
With a = 0,
Then, apply the convolution property.
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 79
10). The Initial- and Final-Value Theorem:
a. If x(t) = 0 for t<0, and x(t) contains no impulses or higher-order singularities at t=0, then
b. If x(t) = 0 for t<0, and x(t) has a finite limit as , then
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 80
a. If x(t) = 0 for t<0, and x(t) contains no impulses or higher-order singularities at t=0, then
Proof: Use Taylor expansion
4. Properties of Laplace Transform (Ch. 9.5)
Using

## Slide 81
Example 9.16:
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 82
Table 9.2 for Laplace transform pairs:
Why don’t we have Laplace transform for signals like
For x(t) = 1, we can write it as x(t) = u(t) + u(-t).
The intersection of the two ROC’s is empty.
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 83
Summaries:
1. Understanding each property: how the time change affects both X(s) and its ROC;
2. Flexible usage of the properties:
Computing LT, inverse LT
Determine the ROC
LTI system analysis
……
4. Properties of Laplace Transform (Ch. 9.5)

## Slide 84
Extra examples: Inverse LT with term
Time shifting property

## Slide 85
Extra examples: Inverse LT with term
The series expansion should be done within ROC.

## Slide 86
Extra examples: Inverse LT with term

## Slide 87
Group discussion:
1. The pole-zero plot is given for a causal system H(s) with
2. It is given that and is of finite duration with no zeros. The number of poles for X(s) is ( ).
The system function can be determined to be ( ).

## Slide 88
5. Analysis of LTI systems using LT
H(s)
LTI
Requirements:
Comprehensive understanding and application of knowledge about LT.
Determine the input X(s) plus it ROC: …
Determine the system function H(s) and its ROC: …
Y(s) and its ROC, the inverse LT for y(t)
Key is flexible usage of LT and ROC properties.

## Slide 89
1). ROC from Causality property:
The ROC associated with the system function for a causal system is a right-half plane.
The converse of this statement is not necessarily true as illustrated in Ex. 9.19 unless for rational system functions.
h(t) = 0 for t < 0
For rational system functions, causality for the system is equivalent to the ROC being the right-half plane to the right of the rightmost pole.
5. Analysis of LTI systems using LT
Anti-causal:
h(t) = 0 for t > 0

## Slide 90
Example 9.17:
Example 9.18:
Rational system function plus ROC being a right-half plane, thus the system is causal.
5. Analysis of LTI systems using LT

## Slide 91
Example 9.19:
Though ROC being a right-half plane, the system function is not rational. So, can NOT determine whether the system is causal or not.
NOT causal from h(t).
Use time shifting property of Laplace transform,
Instead, try to find h(t) first.
5. Analysis of LTI systems using LT

## Slide 92
2). ROC from Stability property:
a. An LTI system is stable if and only if the ROC of its system function H(s) includes the entire jω-axis. (No matter whether the system function is rational or not.) Then, the Fourier transform H(jω) exists.)
b. A causal system with rational system function H(s) is stable if and only if all the poles of H(s) lie in the left-half of the s-plane – i.e., all of the poles have negative real parts.
5. Analysis of LTI systems using LT

## Slide 93
Example 9.20:
Two poles and three possible ROC’s:
(1). Re{s} > 2;
(2). Re{s} < -1;
(3). -1<Re{s} < 2
5. Analysis of LTI systems using LT
For each ROC, causal or stable?

## Slide 94
Example 9.20:
(1). Re{s} > 2:
Both terms are causal, but the second one is the reason for the system to be not stable.
Causal: rational and right ROC
Not stable: ROC not including jω-axis
Partial fraction expansion:

## Slide 95
Example 9.20:
(2). Re{s} < -1: not causal (anti-causal) and not stable
(3). -1 < Re{s} < 2: not causal, but stable

## Slide 96
Take Laplace transform of both sides,
Basis of LT analysis on LTI system described by constant-coefficient differential equations.
5. Analysis of LTI systems using LT
Ch. 2/4:
time and frequency-domain

## Slide 97
Rational form determined by poles and zeros except for a constant factor.
However, no ROC can be derived from the differential equation. If at initial rest, then the system is causal and the ROC is the right plane to the right of the rightmost pole.
5. Analysis of LTI systems using LT
Poles determined with possible ROC’s

## Slide 98
Example 9.23:
Find its impulse response.
ROC ?
(1) Causal, right ROC, Re{s} > -3,
One pole at s = -3, two possible ROC’s.
(2) Anti-causal, left ROC, Re{s} < -3,

## Slide 99
Example 9.24: A series RLC circuit with initial rest
5. Analysis of LTI systems using LT

## Slide 100
Group discussion:
1. A rational system with only two poles at s = -1 and s = +1 plus the information that the output y(t) = 2 when input x(t) = 1. Determine which one of the following choice ( ) is true.
2. A system with real and causal h(t) and two poles for rational H(s) with one at s = -1+j. For system , determine which one of the following choice ( ) is true.
(a) Causal and stable
(b) Causal and not stable
(c) Not causal but stable
(d) Not causal and not stable
(a) Causal and stable
(b) Causal and not stable
(c) Not causal but stable
(d) Not causal and not stable

## Slide 101
Example 9.25: given
Find its system function and write out the differential equation.
ROC?
5. Analysis of LTI systems using LT

## Slide 102
Example 9.25:
The overlap of the ROC’s of X(s) and H(s) should be the ROC of Y(s). So, the only possible choice is then
ROC: two poles at s = -1 and s = -2, three possible ROC’s.
5. Analysis of LTI systems using LT
Note: why this pair of input-output signal can be used to determine the system by using Laplace transform?

## Slide 103
Example 9.26:
The system is causal.
The system function is rational and has only two poles at s = -2 and s = -4.
If x(t) = 1, then y(t) = 0.
The value of the impulse response at t = 0+ is 4.
Given the following information, determine the LTI system:
5. Analysis of LTI systems using LT

## Slide 104
Example 9.26:
2. The system function is rational and has only two poles at s = -2 and s = -4.
1. The system is causal.
3. If x(t) = 1, then y(t) = 0.
Cannot apply H(s) = Y(s)/X(s) as Example 25,
x(t) = 1 has no LT, plus y(t) = 0 gives Y(s) = 0 !
The ROC is a right ROC.

## Slide 105
Example 9.26:
Thus, s = 0 is a zero for H(s). Re-write H(s) as
4. The value of the impulse response at t = 0+ is 4.

## Slide 106
Example 9.27:
Consider a stable and causal system. Its H(s) is rational, contains a pole at s = -2, and does not have a zero at the origin. The location of other poles and zeros is unknown.
For each of the following statement, determine whether it is true, or false, or can’t determine.
What can we say from above facts?
One pole at s = -2 plus causal, boundary of the ROC.
Stable, the ROC includes Re{s} = 0.
Rational and causal, a right ROC.

## Slide 107
Example 9.27:
Need to know whether the ROC of Y(s) for the new signal y(t) = h(t) e3t includes the jw-axis.
F{h(t) e3t} converges.
However, the original ROC is no larger than Re{s} > -2, thus the ROC for the new singal is no larger than Re{s} > 1.
Answer: False.

## Slide 108
Example 9.27:
(b)
Answer: False.
What is this? A zero
(c) th(t) is the impulse response of a causal and stable system.
ROC is not changed, still stable.
H(s) is rational, differentiation in s-domain is still rational, with a right ROC, so still causal.
Answer: True.
Question: Can you obtain the same answer from the time-domain properties of impulse response?

## Slide 109
Example 9.27:
(d) dh(t) /dt contains at least one pole in its LT.
Answer: True.
(e) h(t) has finite duration.
Answer: False. If it is of finite duration, the ROC should be the entire s-plane.
No pole-zero cancellation at s = -2, still one pole.

## Slide 110
Example 9.27:
Answer: Can NOT determine.
(f) H(s) = H(-s).
s = -2 is a pole, then s = 2 is also a pole. For the system to be causal, the (right) ROC should NOT be larger than Re{s} > 2. However, this violates the stable condition.
(g)
Answer: False.

## Slide 111
Summaries:
Comprehensive understanding and application of knowledge about LT.
1. Determine the input X(s) and its ROC: …
2. Determine the system function H(s) and its ROC: …
zeros, poles; differential equations;
given special input-output pair;
if x(t) = 1, y(t) = 0
causal, stable
4. Y(s) and its ROC, inverse LT for h(t)
5. Analysis of LTI systems using LT

## Slide 112
Exercise 9.49: Minimum-delay or minimum-phase system
A class of systems which are causal and stable and the inverse systems are also causal and stable.
5. Analysis of LTI systems using LT
Conclusion:
For such class of systems, all poles and zeros of the transfer function must be in the left half of the s-plane.
Systems:
Inverse systems:

## Slide 113
Group discussion:
1. For a 2nd-order lowpass Butterworth filter designed as
Confirm that the system is both causal and stable.
2. For a system with
For the system, determine which one of the following choice ( ) is true.
(a) Causal and stable
(b) Causal and not stable
(c) Not causal but stable
(d) Not causal and not stable

## Slide 114
6. System Function Algebra and Block Diagram
Basic requirements:
Can derive the system function from the system block diagram;
Several equivalent block diagrams are possible. Given a system function in rational form, can draw a block diagram, especially the direct-form.
Location of poles plus causal and stable properties
Inter-connection of sub-systems

## Slide 115
Interconnections of LTI systems:
1) Determine the input and output of the system;
2) Decompose the system into subsystems, and find the input-output relationship for each subsystem;
3) Obtain the overall input-output relationship.
6. System Function Algebra and Block Diagram

## Slide 116
6. System Function Algebra and Block Diagram
ROC? Causal or stable?
Convolution property and linear property: ROC no change
Series:
Parallel:
Plus, location of poles not change. Still right-sided ROC for causality and still ROC include the jw-axis for stability

## Slide 117
Get rid of Z(s), we have
ROC: If the two subsystems are causal, the whole system will be causal. But, location of poles will change. ROC determined by new rightmost pole.
6. System Function Algebra and Block Diagram
Feedback:
ROC? Causal or stable?

## Slide 118
Location of poles might change completely.
Feedback system
Unstable.
Examples:
Stable.

## Slide 119
Basic elements:
adder
multiplication by a coefficient
integrator
Examples 9.28 9.29 9.30 9.31
6. System Function Algebra and Block Diagram

## Slide 120
Examples 9.28：
6. System Function Algebra and Block Diagram

## Slide 121
Examples 9.28：
6. System Function Algebra and Block Diagram
Adder:
Note: No ROC is given here. The ROC is determined by new poles.

## Slide 122
Examples 9.29：
6. System Function Algebra and Block Diagram

## Slide 123
Examples 9.30：
6. System Function Algebra and Block Diagram

## Slide 124
Examples 9.30：
6. System Function Algebra and Block Diagram

## Slide 125
Examples 9.31：

## Slide 126
Examples 9.31：
6. System Function Algebra and Block Diagram

## Slide 127
Group discussion:
1. The following system function is for a causal system, its unit impulse response is ( )
2. Draw a system block diagram for the following system in direct form.

## Slide 128
7. Unilateral Laplace transform
Including integration of impulses at t = 0 etc.
Basic requirements:
Concept of UL and its difference from bilateral LT
Time-differentiation property of UL and its application

## Slide 129
Including integration of impulses at t = 0 etc.
ROC: always a right-half plane.
If x(t) = 0 for t < 0, then its unilateral LT is identical to the bilateral LT; otherwise, they might be different.
7. Unilateral Laplace transform

## Slide 130
Example 9.33:
Solution: for bilateral LT,
Find the bilateral and unilateral LT for

## Slide 131
Example 9.34:
Solution:
Find unilateral LT.
Including impulses at t = 0
For impulse:
For unit-doublet:

## Slide 132
Properties: similar to the bilateral transform (Here, we focus on the differences. )
Convolution: If x1(t) = 0 and x2(t) = 0 for t<0, then
Differentiation:
7. Unilateral Laplace transform

## Slide 133
Example 9.37: Solving a causal LTI system described by differential equations together with the condition of initial rest
with
7. Unilateral Laplace transform

## Slide 134
Unilateral Laplace transform can be used to Solve differential equations with nonzero initial conditions.
Importance: the system is not at initial rest now, thus not LTI, and can NOT be described uniquely by h(t).
Example 9.38:
with
and
Find the output y(t).
7. Unilateral Laplace transform
for 2nd-order equation

## Slide 135
Take UL transform,
Example 9.38:
7. Unilateral Laplace transform

## Slide 136
Zero-state response
Zero-input response
7. Unilateral Laplace transform
For

## Slide 137
Extra examples: circuit analysis using LT
Point A:

## Slide 138
Point B:
An ideal amplifier:

## Slide 139
Extra examples: circuit analysis using LT
Analysis on stability: 2nd-order system
If , two complex poles in conjugate pair, its real part is , or
Two poles at:

## Slide 140
If
No amplification in the circuit, must be stable.
If , two real poles with
If ,

## Slide 141
Extra examples: LC with non-zero initial condition
Capacitor:
Inductor:

## Slide 142
1. Concept of Laplace transform: extension of FT to the complex domain
Commonly-used FT pairs:
LTI system:
Convergence: ROC determined by real part of s, pole-zero plot
Summary
If …,

## Slide 143
Summary
2. ROC properties:
3. Inverse LT
(1) Four types of time-domain signals, four types of ROC
(2) ROC determined by poles, how to determine the ROC from possible ROC’s
Inverse LT based on partial fraction expansion

## Slide 144
Summary
4. Properties of LT: be careful of ROC change

## Slide 145
Summary
6. System Function Algebra and Block Diagram
7. Unilateral Laplace transform
(1) Concept of unilateral LT and difference from bilateral LT
(2) Solving differential equations with non-zero initial conditions
(1) Series, parallel, feedback interconnection: ROC? Causal? Stable?
(2) Block diagram: system function
5. LT-based system analysis
(1) Causal or stable property determined from ROC
(2) Systems of linear constant-coefficient differential equations
(3) Flexible usage of LT properties

## Slide 146
Group discussion:
1. The unilateral LT for signal is ( )
2. The signal for the following unilateral LT is ( ) .